## Slide 1: RESULT ORIENTED MILLING EFFORTS

## Slide 2: OBJECTIVE OF MILLING
Milling is not only to crush the sugar cane, it is the art of gaining maximum possible extraction of sugar cane avoiding the extraction of non sugars, allowing minimum sucrose and moisture in final bagasse by utilizing the optimum energy.

## Slide 3: FACTORS INFLUENCING MILLING OPERATION
  CANE PREPARATION
  ROLLER GROOVING
  MILL SPEED
  MILL SETTING
  DONNELY CHUTE SETTING
  THE PRESENTATION MAINLY DISCUSS:
  HYDRAULIC LOAD
  IMBIBITION

## Slide 4: HYDRAULIC LOAD DISTRIBUTION IN THE MILL

## Slide 5
FREE JUICE EXTRACTED
ᵩ
β
NEUTRAL PLANE
STATIONARY POOL FREE JUICE
AUXIAL PLANE
DYNAMIC COMPRESSION OF FIBER

## Slide 6
ROLLER SIZE 42” X 84”
HYDRAULIC PRESSURE 172 kg / cm2
FORCE EXERTED BY ROLLER ON BAGASSE
459 TONS
HYDRAULIC PRESSURE
186 kg / cm2
FORCE EXERTED BY ROLLER ON BAGASSE
427 TONS
LOOSE BAGASSE LAYER 470 MM AND MILL FEED OPENING 65 MM AT REST.
JOURNAL SIZE 530 X 670
54 Kg/Cm²
59 Kg/Cm²

## Slide 7
Chart: Impact of Hydraulic Pressure
| HYDRAULIC PRESSURE (Kg/Cm²) | LOAD ON JOURNAL (Kg/Cm²) | ROLLER FORCE (Tons)
Case-1 | 172 | 54.1726 | 426.9928
Case-2 | 186 | 58.582 | 458.8992

## Slide 8: FORMAL IMBIBITION PRACTICE
      Bagasse retains 45% juice not extractable by mechanical means, since this juice cannot be extracted, the efforts are made to replace it with water or low brix juice, this process is termed as imbibition.
      The extraction depends on the ratio of applied water to the fiber, not to the quantity of applied water
      The formal distribution is operating in the plane longitudinal to the delivery rollers nip of the rollers since part of the bagasse adheres to the top roller this allows the water to reach in the mid layer of the bagasse.

## Slide 9
Chart: Relation of Imbibition & LMJ Bx
| 44908 | 44909 | 44910 | 44911 | 44912 | 44913 | 44914 | 44915 | 44916 | 44917 | 44918 | 44919 | 44920 | 44921 | 44922 | 44923 | 44924 | 44925 | 44926 | 44927 | 44928 | 44929 | 44930 | 44931
Imbibition % | 43.65 | 43.45 | 43.92 | 44.92 | 44.51 | 43.27 | 43.27 | 43.98 | 44.11 | 44.05 | 44.99 | 44.49 | 45.22 | 46.04 | 46.12 | 47.02 | 47.27 | 46.74 | 46.14 | 45.97 | 46.17 | 46.1 | 46.23 | 46.62
LMJ Bx | 1.65 | 1.67 | 1.65 | 1.67 | 1.68 | 1.7 | 1.67 | 1.65 | 1.64 | 1.63 | 1.64 | 1.65 | 1.62 | 1.62 | 1.62 | 1.6 | 1.62 | 1.63 | 1.64 | 1.63 | 1.63 | 1.63 | 1.64 | 1.64

## Slide 10
NOZZLE PITCH = 50 mm
NOZZLE DIA = 6 mm
NOZZLE ANGLE = 27ᵒ

## Slide 12
Chart: LMJ Bx & Imbibition Comparison
| 44956 | 44957 | 44958 | 44959 | 44960 | 44961 | 44962 | 44963 | 44964 | 44965 | 44966 | 44967 | 44968 | 44969 | 44970 | 44971 | 44972 | 44973 | 44974 | 44975 | 44976 | 44977
Imbibtion % Cane | 45.73 | 43.99 | 43.43 | 43.44 | 43.42 | 44.64 | 45.39 | 46.49 | 46.67 | 47.17 | 47.24 | 46.75 | 47.18 | 47.19 | 47.44 | 47.52 | 47.25 | 47.25 | 47.28 | 47.28 | 47.43 | 48.02
LMJ Bx | 1.65 | 1.65 | 1.66 | 1.65 | 1.67 | 1.69 | 1.65 | 1.71 | 1.72 | 1.69 | 1.7 | 1.7 | 1.69 | 1.7 | 1.8 | 1.84 | 1.84 | 1.83 | 1.83 | 1.85 | 1.81 | 1.81

## Slide 13
BAGASSE
MOISTURE = 54.00 %
FIBER = 43.00 %
BRIX = 3.00 %
Water/Fiber (W/F) Ratio = 1.256
W/F Ratio = 3.186
1.256 + 3.186 = 4.442 W/F
W/F = 7.0
55.465 % of Layer
SATURATION OF FIBER
BAGASSE
MOISTURE = 80.59 %
FIBER = 18.14 %
BRIX = 1.27 %
Water/Fiber (W/F) Ratio = 4.442

## Slide 14: EFFICIENT IMBIBITION PRACTICES
  Additional point of imbibition water before the last mill is provided under the discharge scrapper, striking the bagasse bottom layer
  One additional point is provided at the apex of bagasse carpet splits into the inter carrier.
  Imbibition water distribution
  On Trash plate nozzles = 50 Tons
  Under the trash = 30 Tons
  Bagasse surface = 60 Tons
  Split bagasse point = 20 Tons

## Slide 15: MAXIMUM ALLOWED IMBIBITION ON FIBRE % CANE
Cane crushing in kg/h | 458 | @ 11000 TCD
Water temperature in Cᵒ | 60 | 
Fiber % cane | 14.27 | 
Peripheral speed of mill roller | 15.7 | Roller diameter 1060 mm
Maximum imbibition of fiber % cane | 364 | 320

## Slide 16
Chart: Season Comparison of Mill Ext and Imbibition % Cane
| December | January | February | Final
2022-23 (Mill Ext Mittal) | 96.796 | 96.843 | 96.828 | 96.82
2021-22 (Mill Ext Mittal) | 96.712 | 96.681 | 96.643 | 96.672
2022-23 (Imb %) | 44.09 | 46.261 | 46.646 | 45.465
2021-22 (Imb %) | 46.236 | 44.94 | 46.347 | 46.489

## Slide 17: CONSEQUENCE OF ALTERING MILLING STRATEGY
SEASON | 2021-22 | 2022-23 | REMARKS
Average cane crushing in TCD | 7625 | 8391.5 | + 10 %
Mill extraction | 96.30 | 96.34 | + 0.04
Bagasse pol % | 1.53 | 1.44 | - 5.88 %
Bagasse moisture % | 51.7 | 51.63 | - 0.14 %
Imbibition % | 46.49 | 45.46 | - 2.2 %

## Slide 18: QUESTIONS CORRELATED TO THE PRESENTATION