## Slide 1: PSST CONVENTION 2023 KARACHI Capacity, efficiency & value additions An experience at JK Sugar Mills Unit -1
Presented by Mohammad Sarfaraz Khan General Manager (JK Sugar Mills Unit-1 Mian Channu) Former Vice President (Engineering) PSST (2017-19)

## Slide 2: Introduction
Current capacity 12000 TCD
3 times enhancement in 5 years
33 years back inception with 4000 TCD
Acquire 2017 by
JK regime on design capacity
Core
Agriculture development to improve business
sustainability
Scope
Capacity, energy efficiency &
Quality Sugar production with HSE compliance to projects corporate sector

## Slide 3: Plant Statistics
Recovery Trend Avg (%)
Since inception 9.17 (33 Years)
Since JK regime 9.62 (6 Years)
Last two season 10.06 Average
Cane Crushed
0.963 MMT (22-23)
1.046 MMT (21-22)
Production
96,288 MT (22-23)
106,128 MT (21-22)

## Slide 4
Chart: 
| 2020-21 | 2021-22 | 2022-23
Survey (Acres) | 53452 | 46469 | 49001
Cane Crushed (MT) | 824915 | 1046482 | 963578
Ratio (Tons/Acre) | 15.43 | 22.52 | 19.66
Comparison of Survey Vs procured Cane (3-years data)
Notes: E-survey, Recult, Farmdar

## Slide 5: Sample 4
Sugar Cane Yield
Pest Management challenges & optimized field measures
Inflict Considerable Loss
Pest Intensity
Awareness of IPM
Sustainability
15 % loss in recovery
20 % declines
103 associated insects with Sugarcane crop
Yield and recovery can improve with timely application of Pest management activities
Integrated & committed coordination with growers from Mills management
Measures being taken after season 2020-21 when pest-intensity massively effected the crop especially white fly, Pyrilla in area and resultant over all recovery remained 8.82%.
Therefore, after coordination at IPM-Cane-Mills & growers level things gets stabilize with application of drones as value addition. Significantly, 10.06% dual season average recovery has been achieved.
IPM initiates & Year wise recovery trend
2020-21 8.82% Intensive pest
2021-22 10.13% Pest control activities
2022-23 10.00% IPM control measures
Notes: Its pure technicalities and expertise job which needs an acute attention and time devotion. However, timely measures can avoid severe loss. Varietal limitations CPF 246 & SPF 234 effected with Red-rot diseased. While SPF 238 and NSG 59 reflects low recovery constrains. Major contributor of losses are Sugar cane Top borer, Gurdas pur borer, Root borer and pink borer as chewing pest. While, sucking pest Pyrilla, white fly, black bug, mealy bug and mites.

## Slide 6
Chart: COMPARISON OF VARIETAL PROCUREMENT (%)
| CP -77400 | NSG-59 | CPF-246 | SPF-234 | HSF-240 | CPF-253
2019-20 | 16.94 | 0.27 | 47.81 | 16.46 | 1.7 | 0
2020-21 | 29.49 | 18.09 | 16.82 | 4.87 | 1.06 | 0.28
2021-22 | 42.66 | 30.21 | 11.67 | 5.83 | 2.83 | 2.4
2022-23 | 45 | 22.3 | 8.9 | 7 | 1.3 | 11.6
Average | 33.52 | 17.71 | 21.3 | 8.54 | 1.72 | 3.57
Notes: 86.36% major contribution . Fortunately an induction of new variety YTFG-236 from Fatima group has been approved by Punjab Govt is committed effort from Mill side.

## Slide 7
Notes: Two sets of cutter with one HD cane shredder (3 MW turbine driven)

## Slide 8: Significance of cane density over capacity rise
Chute level
Bulk density can be increased at the bottom of feed chute by increasing pressure on prepared cane height which is an established relationship projected to 400 - 450 Kg/M3
Cane density (Kg/M3)
After 2 set of knives 300
After HD Shredder &
at first mill chute 400
Capacity utilization
80.015% (21-22)
88.268 % (22-23)

## Slide 9
Chart: 
Chart: 
Chart: 
Chart: 
Mill Extraction (Plain) |  | Mill Extraction (Mittal) |  | Mill Extraction (Deer) |  | Average Cane Crushing (With Stoppages) |  | Average Cane Crushing (Without Stoppages) |  | Imbibition On Cane % | 
2021-22 | 2022-23 | 2021-22 | 2022-23 | 2021-22 | 2022-23 | 2021-22 | 2022-23 | 2021-22 | 2022-23 | 2021-22 | 2022-23
95.741 | 95.121 | 96.081 | 95.058 | 96.041 | 94.885 | 7531.238 | 9265.173 | 8401.621 | 9718.386 | 34.626 | 30.3813
Chart: 
| Mills Extraction (Plan)
2021-22 | 95.741
2022-23 | 95.121
Chart: 
Chart: 
Chart: 
| Mills Extraction (Mittal)
2021-22 | 96.081
2022-23 | 95.058
Chart: 
| Mills Extraction (Deer)
2021-22 | 96.041
2022-23 | 94.885
Chart: 
| Average Cane Crushing (With Stopages)
2021-22 | 7531.238
2022-23 | 9265.173
Chart: 
| Average Cane Crushing (Without Stopages)
2021-22 | 8401.621
2022-23 | 9718.386
Chart: 
| Imbibition on Cane %
2021-22 | 34.626
2022-23 | 30.3813
Mill Extraction, Capacity enhancement with comparative imbibition
Notes: 15.67% average rise 2022-23 crushing capacity

## Slide 10
Chart: 
| 2020-21 | 2021-22 | 2022-23
1st Mill Juice purity | 78.116 | 79.864 | 78.116
Last Mill Juice purity | 67.374 | 69.163 | 68.865
Purity Drop | 10.742 | 10.701 | 9.251
Java Ratio | 78.021 | 81.644 | 80.731
Imbibition % Cane | 0.34212 | 0.34626 | 0.30381
Mills Extraction (Plain) % | 95.412 | 95.741 | 95.121
Comparison of purity drop Vs Extraction (Three – Years)

## Slide 11
Chart: 
Chart: 
Chart: 
Chart: 
Cane Crushing (MT) |  | Steam % Cane |  | Capacity Utilization % |  | Bagasse Saving (MT) |  | Bagasse Saving % |  | Boiler Efficiency % | 
2021-22 | 2022-23 | 2021-22 | 2022-23 | 2021-22 | 2022-23 | 2021-22 | 2022-23 | 2021-22 | 2022-23 | 2021-22 | 2022-23
1046842.10 | 963578 | 44.63 | 40.64 | 80.015 | 88.268 | 28711.481 | 38232.544 | 9.37 | 13.94 | 75.86 | 77.01
Chart: 
Comparison of Capacity Utilization Vs Steam on Cane & Bagasse Saving with Boiler efficiency
(2021-22 & 2022-23)
Chart: 
| Steam % Cane
2021-22 | 44.63
2022-23 | 40.64
Chart: 
| Capacity Utilization
2021-22 | 80.015
2022-23 | 88.268
Chart: 
| Bagasse Saving (M.Tons)
2021-22 | 28711.481
2022-23 | 38232.544
Chart: 
| Bagasse Saving %
2021-22 | 9.37
2022-23 | 13.94
Chart: 
| Cane Crushing (M.Tons)
2021-22 | 1046842.1
2022-23 | 963578
Chart: 
Chart: 
| Boiler Efficiency
2021-22 | 0.7586
2022-23 | 0.7701
Notes: 1.15% efficiency rise

## Slide 12
Chart: 
| Boiler Flue Gases Temp. °C
2021-22 | 220
2022-23 | 197.843
Chart: 
| Bagasse Saving MT
2021-22 | 28711.481
2022-23 | 38232.544
Chart: 
| Economizer Outlet Water Temp. °C
2021-22 | 115.686
2022-23 | 124.3
Chart: 
| Steam Generation (M.Tons)
2021-22 | 4297
2022-23 | 3813
Boiler Flue Gases Temp. °C |  | Bagasse Saving (MT) |  | Economizer Outlet Water Temp. °C |  | Steam Generation (MT) | 
2021-22 | 2022-23 | 2021-22 | 2022-23 | 2021-22 | 2022-23 | 2021-22 | 2022-23
220 | 197.843 | 28711.481 | 38232.544 | 115.68 | 124.3 | 4297 | 3813
Comparison of flue gases Vs inlet temp 2021-22 Vs 2022-23 (Season Avg)
Notes: 22.16 OC temperature reduction leads to 4.54% bagasse saving increase. However, 8.62OC feed water temp rise averagely for the season.

## Slide 13
Condensate quality ensures through RO and subsequent return energy @ 1-3% fuel savings. However, un controlled water chemistry leads to carry overs and ultimately deposition at boilers internals & prime movers too.
Once depositions gets establish 5% turbine efficiency along with 20% capacity drop to be realize.
Induction of RO & impacts over water chemistry & condensate availability

## Slide 14
Chart: 
| Boiler Water TDS
20-21 | 578
21-22 | 504
22-23 | 486
Chart: 
| Feed Water TDS
20-21 | 14
21-22 | 18
22-23 | 12
Chart: 
| Sensible Heat Loss Via Blow Down (K.Cal/Kg of Bagasse)
20-21 | 15.6
21-22 | 13.9
22-23 | 12.3
Chart: 
| Feed Water Quantity required to coup up Kg / Kg of Steam
20-21 | 1.032
21-22 | 1.029
22-23 | 1.025
Chart: 
| NCV Energy Loss Via Blow Down (%)
20-21 | 0.89
21-22 | 0.79
22-23 | 0.7
Chart: 
| Blow Down quantity kg / kg of Steam loss
20-21 | 0.032
21-22 | 0.029
22-23 | 0.025
Boiler Water Chemistry Vs Boiler Energy Loss

## Slide 15: Energy & Power consumption Vs quality Production (Value addition)
Chart: 
| Steam on Cane(%) | Power (KW/Ton of cane) | Quality Sugar production(%)
Season 2021-22 | 44.63 | 18.73 | 29.09
Season 2022-23 | 40.64 | 17.5 | 34.77
Notes: Corporate sector

## Slide 16: In-efficient Sanitation contributes sugar loss
Chart: 
| Acid Inversion | Enzymatic Inversion | Microbial Infections | Cumulative Impact of sucrose loss (Kg/Ton of cane) | Efficient sanitation can reduce sucrose loss 0.9 (Kg/ton of cane)
Series 1 | 0.16 | 0.22 | 0.62 | 2.5 | 0.9

## Slide 17: “Control Measures” State of Sanitation (Proportionate purity ratios / ERQV values) Comparison values for MJ/PJ 98% for an excellent while 95-97% satisfactory Comparison values for LMJ/PJ 85% for an excellent while 83-84% satisfactory
Chart: 
| ERQV MJ/PJ | ERQV LMJ/PJ
Season 2021-22 | 0.9963 | 0.7315
Season 2022-23 | 0.9788 | 0.73008
Notes: Bleaching powder at shredded cane, (Anti-bacterial), Biocide at last Mill, Application of hot water twice a shift preceded by jet of steaming

## Slide 18: Corporate compliance (Value additions 2021-23)
Standard certifications, Quality & Sustainability
QMS ISO 9001 - 2015
FSSC 22000 (Version 5.1)
HALAL PS 3733 : 2022
Bonsucro Production standard (Version 5.1)
Bonsucro Mass balance chain of custody (Version 5.1)
Bonsucro production standard for small holder farmers (Version 1.0)

## Slide 19: Environmental Measures (CSR)
Induction of 100 M3/hour effluent treatment plant
To meets NEQS & Corporate Social Responsibility
Treated water reuse at farms and agriculture lands to make sustainability and resultant curtail diesel / electricity costs
Emission compliance as per PEQS

## Slide 20
Parameters | Analysis Method | Unit | LOR | Result 01 | PEQS
pH | APHA-4500-H+B | pH unit | 0.01 | 7.77 | 6-9
Total Dissolved Solid (TDS)** | APHA-2540C | mg/l | 1.0 | 772.0 | 3500
Oil and Grease | USEPA-1664 | mg/l | 0.2 | <0.2 | 10
Biological Oxygen Demand | APHA-5210 B | mg/l | 1.0 | 16.0 | 80
Chemical Oxygen Demand | APHA-5220-D | mg/l | 1.0 | 46.0 | 150
Total Suspended Solids | APHA-2540-C | mg/l | 1.0 | 44.0 | 200
Abbreviations: ND: Not Detected LOR: Limit of Reporting PEQS: Punjab Environmental Quality Standards Note: Temperature 1.5OC while specified limits ≤ 3OC ( Jan 20,2023) |  |  |  |  | 
Waste Water Analysis Season 2022-23

## Slide 21
Stack Emission Monitoring Report (Boiler # 3, 84 TPH capacity) dated Jan 14, 2023
Parameters | Unit | Reading 01 | Reading 02 | Reading 03 | Limits as per PEQS
Carbon Dioxide (CO2) | % | 7.56 | 8.17 | 8.25 | -
Oxygen (O2) | % | 13.02 | 12.58 | 11.85 | -
Carbon Monoxide (CO) | mg/Nm | 141.00 | 158.00 | 163.00 | 800
Sulphur Dioxide (SO2) | mg/Nm | 75.00 | 81.00 | 86.00 | 1700
Nitrogen Dioxide (NO2) | mg/Nm | 12.00 | 17.00 | 22.00 | -
Nitrogen Oxide (NO) | mg/Nm | 208.00 | 217.00 | 231.00 | -
NOx | mg/Nm | 220.00 | 244.00 | 255.00 | -
Smoke | Ringlemann Scale | 1.00 |  |  | 2
Particulate Matter | mg/Nm | 115.30 |  |  | -
Parameters | Unit | Reading 01 | Reading 02 | Reading 03 | Limits as per PEQS
Carbon Dioxide (CO2) | % | 7.56 | 8.17 | 8.25 | -
Oxygen (O2) | % | 13.02 | 12.58 | 11.85 | -
Carbon Monoxide (CO) |  | 141.00 | 158.00 | 163.00 | 800
Sulphur Dioxide (SO2) |  | 75.00 | 81.00 | 86.00 | 1700
Nitrogen Dioxide (NO2) |  | 12.00 | 17.00 | 22.00 | -
Nitrogen Oxide (NO) |  | 208.00 | 217.00 | 231.00 | -
NOx |  | 220.00 | 244.00 | 255.00 | -
Smoke | Ringlemann Scale | 1.00 |  |  | 2
Particulate Matter |  | 115.30 |  |  | -
Notes: All suspended liquid & solid particles present in air reflects the air quality.

## Slide 22: safety compliance at plant (3 -Years comparison) Frequency of Yearly incidents (Numbers)
Chart: 
| 2021 | 2022 | 2023
Near Miss | 49 | 38 | 29
Minor (FAC) | 18 | 13 | 7
LTI | 9 | 7 | 4
Fatality | 0 | 0 | 0

## Slide 23: Conclusion Dual season results reflected plant capacity utilization 80.01 – 88.26% with core perspective to produce quality sugar at optimum energy efficient levels with certification compliance. However, 10.06% average recovery attained with control IPM, Varietal and procurement initiatives against severe white fly, Pyrilla & associated pests effected territory.

## Slide 24: Thank You!