## Slide 1
Sustainable Environment Developers
Formerly known as Spray Engineering Devices
Spent Wash Evaporation
with
MVR Based Plate Type Evaporator
A Saad Masud Presentation At PSST Annual Convention
September 12, 2023

## Slide 2
Product Overview

## Slide 3
The Problem
Disposal of Spent Wash with required COD level is a challenge faced by all Molasses based Distilleries.
  High COD level water is a threat to the environment.
  The local plant operators are searching for the optimum solution with minimum operating cost.
  Keeping in view the above problem SED came up with the following solution which is already in operation.

## Slide 4
The Solution
MVR Based Plate Type Evaporator

## Slide 5
Case Study
Raw Material: Molasses
Capacity: 40,000 Liters/day
Location: Kisumu, Kenya
Operating Days: 365
Other Units in the Complex:
Kibos Sugar Limited - 4500 TCD
Kibos Paper Products – 200 Tons/Day
Kibos Fertilizer

## Slide 6
Process Flow Chart
SPENT WASH
MVR Evaporator
REJECT
CONDENSATE
CONDENSATE
POLISHING
UNIT
KIBOS PAPER
KIBOS FERTILIZER
Steam Turbine
150m3
100Kw/Hr.
80-85m3/day
Condensate Quantity:
80-85m3/day
TDS : 150
COD: 2,000 ppm.
Quantity: 80-85m3/day
TDS : 500
COD: 20 ppm
50 Tons.
Input Brix: 24
Input COD: 250,000ppm
Input TDS: 240,000

## Slide 7
Spent Wash Evaporator

## Slide 8
Spent Wash Evaporator
Condensate Parameters
Quantity: 80-85m3/day
TDS : 150
COD: 2,000 ppm.
Clear water as condensate.
Capacity- 120m3/Day
Operating at 150m3/day
Input Qty : 150m3/day
Input Brix: 24
Input COD: 250,000ppm
Input TDS: 240,000
Reject Parameters:
Quantity: 66m3(50 Ton)
Brix: 55
COD: 800,000ppm
TDS: 550,000
Power Load 100kw/hr

## Slide 9
Spent Wash Evaporator
Looking into the tube side flow direction
Vapour flow path
Solution side

## Slide 10
Compressed Vapour In
Vapor Out
Wastewater In
Clean Water Out
Feed Out
NCG
MVR
Vacuum Pump
PHE
Heating Medium
MVR Based Evaporator
Compressed Vapour In
Vapor Out
Clean Water Out
Wastewater In
Feed Out
MVR
Vacuum Pump
PHE

## Slide 11
Comparison with Pakistan
Spent Wash Parameters | KIBOS Kenya | Pakistan
Input Brix | 24 | 8
Input COD | 250,000 ppm | 30,000 ppm
Input TDS | 240,000 | 80,000
 | Spent Wash Comes Directly from Distillery | Spent Wash come after Bio Methanation
Input Quantity | 400 m3 | 1200 m3

## Slide 12
Proposed Flow Diagram
Condensate
Quantity: 850m3/day
TDS : 75
COD: 200 ppm.
Distillery Spent Wash
Reject
Quantity: 300Tons
Brix: 55
1.2 Mw/hr
Quantity: 650m3/day
TDS : 200
COD: 20 ppm.
Condensate Polishing Unit
Bio Fertilizer/day
Distillery/ Utilities
Steam & Power for Drying
Foam Removal
CPU
MVR
Evaporator
Steam Turbine
1200m3/day
Dryer
100 Tons/day

## Slide 13
Inputs and Outputs
Spent Wash Quantity | 100 m3 / Day
Condensate Water | 55 m3 / Day
Reject | 45 m3 or 34 Tons / day at 55 Brix
Dry Output | 08 Tons / day
A simple estimate … if you have 100m3 of Spent wash
INPUT
OUTPUT
+
Spent Wash
Condensate
Reject

## Slide 14
Objectives…WE can Achieve
Zero Liquid Discharge (ZLD)
Reduced requirement of Fresh Water
Better Crop Quality through organic Fertilizer
Significant Revenues from Sale of Bio Fertilizer
Better relations with Environment Agencies

## Slide 15
Sustainable Environment Developers
Head Office: B-144, Block 11, Gulistan-e-Jauhar, Karachi.  +92-21-34184313  contact@sedl.pk
Factory: C-66, Phase I, S.I.T.E –II, Superhighway, Karachi.  : +92-300-0342650  www.sedl.pk
Let’s Protect the Environment TOGETHER