## Slide 1
MATIARI SUGAR MILLS LTD
DISTILLERY SPENT WASH IS A BIO-NUTRIENTS SUPPLIMENT AND SOIL CONDITIONER.
Presented by: Rao Shafeeque
Manager; Matiari Agriculture Services

## Slide 2
INDUSTRIES & WASTE WATER AT A GLANCE
Industries have generated effluent, some times harmful to environment.
Industries are established to encourage economic growth and create employment.
The nature of industrial waste varies from industry to industry.
Distillery waste water carries huge potential for agriculture support.

## Slide 3
DSW IS AN ASSET
Questions are raised for DSW, against land pollution & quality.
Viable Soil Conditioner
Proved by researchers
World-wide usage as a manure
Growth Hormones & nutrients
Useful Liquid Fertilizer

## Slide 4
DISTILLERY SPENT WASH A BY-PRODUCT OF MOLASSES BASED DISTILLERY
DSW, comprises organic & inorganic substances.
Include very useful quantity of Macro Nutrients.
Consist of adequate amount of Micro Nutrients.
Can potentially enhance the crop growth & improve soil health.

## Slide 5
CHEMICAL CHARACTERISTICS OF DISTILLERY SPENT WASH (DSW)
CHARACTERISTICS | VALUE | CHARACTERISTICS | VALUE
Potassium | 9600 – 17475 | pH | 3.9 - 4.3
Nitrogen | 1660 – 4200 | EC (dS m-1) | 30.5 – 45.2
Phosphorous | 225 – 3038 | COD | 103,000 - 134,000
Calcium | 2050 – 7000 | BOD | 46,100 – 96,000
Magnesium | 1715 – 2100 | Sulphate | 5100
Zinc | 3240 – 3425 | Maganese | 4.6 – 5.1
Copper | 0.4 – 2.1 | Gibberellic acid | 3246 – 4943
Iron | 6.3 – 7.5 | Indole acetic acid | 25 – 61
All the values are given mg L-1 except EC |  |  | 

## Slide 6
COMMERCIAL FERTILIZERS
SUGAR & DISTILLERY WASTES
SUGAR MILL & DISTILLERY WASTE SUBSTITUTE OF COMMERCIAL FERTILIZERS
Skyrocketing prices….
Cheap source of fertilizers.
Acceptable To Soil Organisms
Environment friendly…..
Constantly use to crop & soil…
Makes crop & soil addicted…

## Slide 7
INTEGRATED USE OF SPENT WASH @ MSM FARMS
TOTAL AREA OF PLOT: 3.750 Acres (1.875 Check plot + 1.875 Control plot)
APPLICATION OF DSW: 1,000 liters/Acre (Fertigation with irrigation water)
Total plot area divide into two equally sub-plots | 1.875 | 1.875
Check plot DSW+ Ch. Fertilizers & Control is only Ch Fr | Check | Control
After harvesting weight difference b/w the both plots | 1961 mds | 1509.75 mds
Yield differences per acre (Monds) | 1045.8 | 805.2
Yield increase by DSW+ NPK fertilizers in check plot | 240.6 mds per acre | 

## Slide 8
VIDEO COVERAGE OF DISTILERY SPENT WASH BY FERTI- IRRIGATION METHOD AT MSM FARMS.
VIDEO BEING SHARED ON THE NEXT SLIDE

## Slide 10
MAS
MATIARI AGRICULTURE SERVICES
(MATIARI SUGAR MILL,SINDH)
MSM
MSM